## Slide 1
Zhijian Yang, Romit Roy Choudhury
ACM SIGCOMM 2021
Personalizing Head Related Transfer Functions for Earables

## Slide 2
Imagine you are wearing earphones … and you hear
Notes: Imagine you are wearing earphones … and you hear a voice says

## Slide 3
Imagine you are wearing earphones … and you hear
“Hello, please come this way”
“Hello, please come this way”
Notes: “Hello, please come this way”

## Slide 4
Can you tell if the sound is real or virtual?
Imagine you are wearing earphones … and you hear
“Hello, please come this way”
“Hello, please come this way”
Notes: Do you think you can tell if the voice was played through the earbud … or was it a real person calling you from somewhere nearby?

## Slide 5
Imagine you are wearing earphones … and you hear
With today’s earphones, you easily can.
“Hello, please come this way”
“Hello, please come this way”
Can you tell if the sound is real or virtual?
Notes: With today’s earbud sounds, you can easily tell the difference.

## Slide 6
But is it possible to make the virtual sound indistinguishable with real one?
With today’s earphones, you easily can.
Imagine you are wearing earphones … and you hear
“Hello, please come this way”
“Hello, please come this way”
Can you tell if the sound is real or virtual?

## Slide 7
In other words, can we fool the brain … so it cannot tell the difference ?
Imagine you are wearing earphones … and you hear
With today’s earphones, you easily can.
“Hello, please come this way”
“Hello, please come this way”
But is it possible to make the virtual sound indistinguishable with real one?
Can you tell if the sound is real or virtual?

## Slide 8
In other words, can we fool the brain … so it cannot tell the difference ?
“Hello, please come this way”
“Hello, please come this way”
Can you tell if the sound is real or virtual?
Notes: Imagine you are wearing an earbud … and imagine a voice says “hey you, come here”. Do you think you can tell if the voice was played through the earbud … or was it a real person calling you from somewhere nearby?
With today’s earbud sounds, you can easily tell the difference.
But wait … is it possible to design the voice sound carefully so that you CANNOT tell the difference between the artificial and real one? In other words, can I fool your brain into thinking that the earbud sound is actually a real sound?

## Slide 9
Filter the sound
Sounds real!!
Any voice or sound
This paper aims to design a filter , such that …
In other words, can we fool the brain … so it cannot tell the difference ?
“Hello, please come this way”
“Hello, please come this way”
Can you tell if the sound is real or virtual?
Notes: This paper aims to design a filter, such that when it’s applied on the original sound, it can trick the brain to believe this is an actual sound

## Slide 10
Filter the sound
Sounds real!!
Any voice or sound
This paper aims to design a filter , such that …

## Slide 11
Filter the sound
Sounds real!!
Any voice or sound
This filter is called: Head related transfer function (HRTF)
HRTF research began as early as the 1960s
This paper aims to design a filter , such that …
but HRTF design is still a challenging problem
Notes: People have been using artificially created heads to understand how signals bounce around the head and ear since long ago, but the complex geometry of human anatomy makes this difficult.

## Slide 12
This filter is called: Head related transfer function (HRTF)
but HRTF design is still a challenging problem
1. how the sound bends or diffracts around your cheek and face

## Slide 13
1. how the sound bends or diffracts around your cheek and face
2. how the real signal bounces inside your pinna
HRTF()
If the earbud can learn your personalized HRTF … then fooling your brain is easy.
HRTF filter
Then a lot of applications can be enabled…
This filter is called: Head related transfer function (HRTF)
but HRTF design is still a challenging problem
Pinna
Signal Scattering
Notes: We essentially needed to pass the original sound signal through the HRTF filter, and then a realistic spatial audio can be created.
Then a lot of applications can be enabled…

## Slide 14
Spatial Audio Navigation
If the earbud can learn your personalized HRTF … then fooling your brain is easy.
HRTF filter
Then a lot of applications can be enabled…

## Slide 16
Spatial Audio Navigation
VR Gaming
Virtual Immersive Meeting with 360 Audio
If the earbud can learn your personalized HRTF … then fooling your brain is easy.
HRTF filter
Then a lot of applications can be enabled…

## Slide 17
It is extremely hard to understand how your head and ear affect sound.
How is HRTF measurement performed today?
In very controlled settings.
Acoustic chamber
Difficult to obtain
Spatial audio products are using generic HRTF
Big rotating speaker array
Generic HRTF is not optimal.
Notes: A user is asked to sit in a large acoustic chamber and wear in-ear microphones. A large rotating speaker array can then simulate the sound effect of a sound source at any given angle. In this way, HRTFs can be estimated.
This means, the spatial audio products we see these days, like the apple airpods pro and oculus quest are using global HRTF.
Global HRTF is not optimal. We did our study.

## Slide 18
Generic HRTF leads to as large as 60 degrees externalization error!!
Generic HRTF is not optimal.
We ask user to identify the sound direction.
Notes: We plotted the heatmaps here. In the first heatmap, we plot the self - xcorr between a user’s own HRTF at different angles, which is diagonal. In the second heatmap, we plot the xcorr between a user’s own HRTF and global HRTF, which is obviously not digonal.

## Slide 19
Spatial audio products are using global HRTF
It is extremely hard to understand how your head and ear affect sound.
Generic HRTF leads to as large as 60 degrees externalization error!!
How is HRTF measurement performed today?
In very controlled settings.
Acoustic chamber
Difficult to obtain
Big rotating speaker array

## Slide 20
Can we personalize HRTF without acoustic chamber?
3D scan
Acoustic simulation/ML
Material (skin, hair) property difficult to estimate.
It is extremely hard to understand how your head and ear affect sound.
How is HRTF measurement performed today?
In very controlled settings.
Acoustic chamber
Difficult to obtain
Big rotating speaker array
Notes: Can we personalize HRTF without acoustic chamber?
Previous researchers have used …

## Slide 21
How is HRTF measurement performed today?
In very controlled settings.
Acoustic chamber
Difficult to obtain
Big rotating speaker array
Can we personalize HRTF without acoustic chamber?
3D scan
Acoustic simulation/ML
Material (skin, hair) property difficult to estimate.
It is extremely hard to understand how your head and ear affect sound.
This paper asks: can we build a system allowing easy personalized HRTF estimation at home?
Notes: Can we personalize HRTF without acoustic chamber?
Previous researchers have used …

## Slide 22
Smartphone as transmitter.
In-ear microphone as receiver.
HRTF estimated by rotating phone around the head.
This paper asks: can we build a system allowing easy personalized HRTF estimation at home?
Here is our basic idea for UNIQ:
The remaining slides are organized as following:
UNIQ System Sketch
2 technical parts
  Phone localization
  Near-far HRTF conversion
Implementation & Evaluation
Notes: Here is our basic idea for UNIQ:

## Slide 23
UNIQ: System Sketch

## Slide 24
UNIQ: System Sketch
Use smartphone as a transmitter
Smartphone transmits a known signal 𝑠
Two in-ear microphones receive signals
User moves the phone; IMU records motion
Front
P
(phone)
L
R
Front
P
(phone)
L
R

## Slide 25
Front
P
(phone)
L
R
If we have the precise phone location, then we have near field HRTF
UNIQ: System Sketch
Use smartphone as a transmitter
Smartphone transmits a known signal 𝑠
Two in-ear microphones receive signals
User moves the phone; IMU records motion
Estimate channel h from known s and r
Localize phone using IMU + Mic fusion

## Slide 26
Use smartphone as a transmitter
Smartphone transmits a known signal 𝑠
Two in-ear microphones receive signals
User moves the phone; IMU records motion
Estimate channel h from known s and r
Localize phone using IMU + Mic fusion
Near to far field HRTF conversion
Front
P
(phone)
L
R
Near field is not enough since we want to create the effect for far field
Technical Part 1: Phone Localization
Let’s start with:
UNIQ: System Sketch

## Slide 27
,
Goal: As user rotates the phone around the head,
localize each phone location
Assume we know the distance between mic, and there’s no head
  Then localization is straightforward…
Technical Part 1: Phone Localization
L
R

## Slide 28
Goal: As user rotates the phone around the head,
localize each phone location
Assume we know the distance between mic, and there’s no head
  Then localization is straightforward…
But what happens when there’s a head in between?
  Signal diffracts around head
  To model diffraction, we need head size & shape
Diffraction-aware sensor fusion
,
Technical Part 1: Phone Localization
L
R
Front
(phone)
L
R
Front
L
R
(unknown!)

## Slide 29
,
Goal: As user rotates the phone around the head,
localize each phone location
Assume we know the distance between mic, and there’s no head
  Then localization is straightforward…
But what happens when there’s a head in between?
  Signal diffracts around head
  To model diffraction, we need head size & shape
Diffraction-aware sensor fusion
  Phone IMU gives ->
  Diffraction based trilateration gives ->
  Over-determined: jointly solve for head shape and phone loc.
Technical Part 1: Phone Localization
L
R
Front
(phone)
L
R
Front
L
R
(unknown!)

## Slide 30
By mapping the phone location with the acoustic channel, we get the near field HRTF
We have phone location estimated now.

## Slide 31
Near
Field
Far
Field
But in most of the cases, we will need far field HRTF
Our next module:
  Near field HRTF: coming from a point source
  Far field HRTF: coming from parallel lines
By mapping the phone location with the acoustic channel, we get the near field HRTF
Near - Far Conversion
We have phone location estimated now.

## Slide 32
Technical Part 2:
Near - Far Conversion

## Slide 33
Goal: synthesize the far-field HRTF at angle
, using near field HRTFs on trajectory A
Technical Part 2:
Near - Far Conversion
Far field source
L
R
A (Near field trajectory)

## Slide 34
Technical Part 2:
Near - Far Conversion
L
R
A (Near field trajectory)
Goal: synthesize the far-field HRTF at angle
, using near field HRTFs on trajectory A
Intuition: far field HRTF is a recombination of different rays for near field HRTF at different locations

## Slide 35
Technical Part 2:
Near - Far Conversion
L
R
A (Near field trajectory)
Goal: synthesize the far-field HRTF at angle
, using near field HRTFs on trajectory A
Intuition: far field HRTF is a recombination of different rays for near field HRTF at different locations

## Slide 36
Goal: synthesize the far-field HRTF at angle
, using near field HRTFs on trajectory A
Intuition: far field HRTF is a recombination of different rays for near field HRTF at different locations
L
R
A (Near field trajectory)
Technical Part 2:
Near - Far Conversion

## Slide 37
Goal: synthesize the far-field HRTF at angle
, using near field HRTFs on trajectory A
Intuition: far field HRTF is a recombination of different rays for near field HRTF at different locations
The decomposition for near field HRTF is a difficult problem
See detailed discussions in the paper
Far field source
L
R
A (Near field trajectory)
Technical Part 2:
Near - Far Conversion
We now have the far field HRTF estimated.
UNIQ HRTF
Sounds real!!
Any voice or sound

## Slide 38
Implementation and Evaluation
We implemented UNIQ on COTS mobile devices
Notes: Finally, let me talk about implementation and evaluation. We implemented UNIQ on COTS mobile devices , including a smartphone, speaker, and in-ear microphone.

## Slide 39
Implementation and Evaluation
Notes: We show that UNIQ generates HRTF 1.8x more accurate than global HRTF.
In terms of estimating real world sound AoA, UNIQ can decrease the error of by 3X than if we use a global HRTF.

## Slide 40
Implementation and Evaluation
UNIQ generates HRTF 1.8x more accurate than generic HRTF
More results in the paper
Notes: We show that UNIQ generates HRTF 1.8x more accurate than global HRTF.
In terms of estimating real world sound AoA, UNIQ can decrease the error of by 3X than if we use a global HRTF.

## Slide 41
More details in the paper …
Thanks.
Zhijian
Romit

## Slide 42
We present one application here: binaural AoA estimation
Hearing aids beamforming
Other than making user hear better, what else can personalized HRTF do?

## Slide 43
We present one application here: binaural AoA estimation
Hearing aids beamforming
Sound based user localization
Other than making user hear better, what else can personalized HRTF do?

## Slide 44
We present one application here: binaural AoA estimation
Hearing aids beamforming
Sound based user localization
Other than making user hear better, what else can personalized HRTF do?
binaural AoA estimation
Binaural recording
Estimated HRTF
AoA

## Slide 45
We present one application here: binaural AoA estimation
Hearing aids beamforming
Sound based user localization
Other than making user hear better, what else can personalized HRTF do?
binaural AoA estimation
Binaural recording
Estimated HRTF
AoA
For estimating real world sound direction: UNIQ can decrease the error of by 3X