## Slide 1
I am a Smartwatch and I can Track my User’s Arm
Sheng Shen, He Wang, Romit Roy Choudhury

## Slide 2
Understanding human arm motion
How is the arm moving?
What is the meaning of this motion?

## Slide 3
What is the meaning of this motion?
Gesture Recognition

## Slide 4: Gesture Recognition
Running
Smoking
Drinking
Driving

## Slide 5: Gesture Recognition
Running
Smoking
Drinking
Driving
[WearSys’15]
[MobiSys’14]
[Rithmio]
[WaterMinder]

## Slide 6
How is the arm moving?
What is the meaning of this motion?
Gesture Recognition
Posture Tracking

## Slide 8: Arm Posture Tracking - Applications
Motion Gaming
Healthcare
Sports Analytics
Natural User Interface
Can we track arm postures with a smartwatch alone?

## Slide 9: Can we track arm postures with a smartwatch alone?
What is inside a smartwatch?
Accelerometer
Gyroscope
Compass
Acceleration along 3 axes
Rotation speed around 3 axes
North vector projected to 3 axes
X
Y
Z

## Slide 10: Can we track arm postures with a smartwatch alone?
Elbow
Shoulder
Wrist
Posture = < Elbow Location, Wrist Location, Wrist Rotation >
What do we need to track?

## Slide 11: Can we track arm postures with a smartwatch alone?
Elbow
Shoulder
Elbow Location
3D Sphere (DoF: 2)
What do we need to track?

## Slide 12: Can we track arm postures with a smartwatch alone?
Shoulder
Wrist
Elbow Location
Wrist Location
3D Sphere (DoF: 2)
3D Sphere (DoF: 2)
What do we need to track?

## Slide 13: Can we track arm postures with a smartwatch alone?
Elbow
Shoulder
Wrist
Elbow Location
Wrist Location
Wrist Rotation
3D Sphere (DoF: 2)
3D Sphere (DoF: 2)
1D Angle (DoF: 1)
What do we need to track?

## Slide 14: Can we track arm postures with a smartwatch alone?
Accelerometer
Gyroscope
Compass
Elbow
Shoulder
Wrist
?
Smartwatch = < Accelerometer, Gyroscope, Compass>
Posture = < Elbow Location, Wrist Location, Wrist Rotation >

## Slide 15: Experiment 1: Double Integration (Dead Reckoning)
Gyroscope
Wrist Orientation
sensor fusion
Accelerometer
Compass
Step 1
+
Y
Roll
Z
Yaw
Pitch
X

## Slide 16: Experiment 1: Double Integration (Dead Reckoning)
Step 2
Gyroscope
Wrist Orientation
sensor fusion
Accelerometer
Compass
Step 1
Accelerometer
Global Acceleration
Projection
Linear Acceleration
Gravity Removal
Velocity
Wrist Location
+
Wrist Orientation

## Slide 17: Experiment 1: Double Integration (Dead Reckoning)
Wrist Location
Wrist Orientation
Wrist orientation error is okay…
Wrist location error goes unbounded!
Double integration won’t work in unconstrained space

## Slide 18: Experiment 2: State Estimation
Posture space is indeed constrained
Why not estimate 5 unknowns directly?
Accelerometer
Gyroscope
Compass
Posture
Dimension: 5+5+5=15
Posture = < Elbow Location, Wrist Location, Wrist Rotation >
DoF: 5 = 2 + 2 + 1
The search space is too large for efficient state estimation
Need to find a way to reduce search space!

## Slide 19: What happens if wrist orientation is fixed…
Forearm pointing upward Palm facing towards yourself

## Slide 20: What happens if wrist orientation is fixed…
Elbow
Forearm pointing upward Palm facing towards yourself
Elbow Point Cloud: A subset of elbow sphere

## Slide 21: What happens if wrist orientation is fixed…
Elbow
Wrist
Forearm pointing upward Palm facing towards yourself
Elbow Point Cloud: A subset of elbow sphere
Wrist Point Cloud: A shift of elbow point cloud, along forearm direction

## Slide 22: What happens if wrist orientation is fixed…
Elbow
Wrist

## Slide 23: What happens if wrist orientation is fixed…
Elbow
Wrist
For a fixed wrist orientation, arm posture space is small!
This is promising, as we already estimate wrist orientation reasonably well…
But how can we derive this point cloud for each wrist orientation?

## Slide 24: Human Arm Model
: [-60° ~ 180°]
: [-40° ~ 120°]
Shoulder:

## Slide 25: Human Arm Model
Shoulder:
Elbow:
: [-60° ~ 180°]
: [-40° ~ 120°]
: [0° ~ 150°]
: [0° ~ 180°]

## Slide 26: Human Arm Model
Shoulder:
Elbow:
Elbow Location
Wrist Location
Wrist Orientation

## Slide 27: Human Arm Model
Shoulder:
Elbow:
Elbow Location
Wrist Location
Wrist Orientation
M-N Mapping
1-N Mapping for each orientation

## Slide 28: Orientation – Location Mapping
Elbow Location
Wrist Orientation
Wrist Location
1-N Mapping for each orientation

## Slide 29: Video: Point Cloud Tracking
RGB Video
Kinect Groundtruth
Elbow/Wrist Point Clouds

## Slide 30: How large are the point clouds?
Fraction =
Median: 8.3%

## Slide 31: How large are the point clouds?
Since they are small, what if we simply take an average?
Median Error: (12.0cm, 13.3cm)

## Slide 32: How large are the point clouds?
Since they are small, what if we simply take an average?
What happens if wrist orientation doesn’t change?

## Slide 33: Elbow Location Inferencing
t
Possible Elbow Locations

## Slide 34: Elbow Location Inferencing
t
Possible Elbow Locations

## Slide 35: Elbow Location Inferencing
t
Possible Elbow Locations
Accelerometer
Wrist Acceleration
Projection
Gravity Removal
Wrist Orientation
Wrist-to-Elbow Acceleration
Forearm Rotation
Elbow Acceleration

## Slide 36: Elbow Location Inferencing
t
Possible Elbow Locations
Elbow Acceleration
Location
Velocity
Acceleration
State 1

## Slide 37: Elbow Location Inferencing
t
Possible Elbow Locations
Elbow Acceleration
Location
Velocity
Acceleration
State 2

## Slide 38: Elbow Location Inferencing
t
Possible Elbow Locations
Elbow Acceleration
Location
Velocity
Acceleration
Transition 12
HMM & Viterbi gives optimal solution!

## Slide 39: Viterbi Decoding
T Time Steps
N Possible Elbow Locations
State (2 Locations)
Velocity
Acceleration (Transition)
Acceleration (Observation)
Transition Prob.

## Slide 40: Evaluation
Median Error: (7.9cm, 9.2cm)
Elbow: 12.0cm  7.9cm
Wrist: 13.3cm  9.2cm

## Slide 41: Video: Write in the Air

## Slide 42: Limitation
Facing direction - Need to express arm posture in torso coordinate system
Tracking on the move - Body motion will pollute accelerometer signal
Speed - Need improvement

## Slide 43: Conclusion
Tracking arm postures using motion sensors on a smartwatch alone
Fusing observations from human kinematics and IMU sensors into a HMM
<7.9cm, 9.2cm> tracking error for <elbow, wrist>