## Slide 1
EarSense: Earphones as a Teeth
Jay Prakash
Zhijian Yang, Yu-Lin Wei, Haitham Hassanieh and Romit Roy Choudhury
Activity Sensor
Notes: 1. Good Evening, I am Jay … a visiting PhD student at UIUC. I am doing my PhD from SUTD, Singapore.
I would like to introduce our research Earsense … which was conceptualized with a vision of exploiting teeth as an activity sensor.

## Slide 2
Basis of EarSense
Maxilla
Mandible
Zygoma
Vibrations from the teeth conduct through skull and arrive at eardrum.
Notes: 2. Earsense is based on the premise that … vibrations generated from human teeth … would conduct through the jaw and skull bones … and eventually arrive at the eardrum.

## Slide 3
Can off-the-shelf earphones
sense these surface vibrations?
1
This paper asks:
Notes: 3. This paper asks two questions:
One … can today’s off-the-shelf earphones be used to pick up the vibration signal?

## Slide 4
Can off-the-shelf earphones
Sense these surface vibrations?
Can vibration signals be analyzed
to infer gestures and source locations?
1
2
This paper asks:
Teeth Gesture,
Location
Infer
Left
signal
Right
signal
Infer
Left
signal
Notes: 4. And two … can we analyze these vibrations … and infer the actions or gestures of the teeth … and even the teeth locations where such gestures were made

## Slide 5
Why?
Notes: 5. Before describing details, an obvious question arises … Why should we care?

## Slide 6
Teeth Gesture,
Location
Infer
Left
signal
Right
signal
Range of Applications …
Notes: 6. We envision a wide range of applications from healthcare to user interfaces

## Slide 7
Teeth Gesture,
Location
Infer
Left
signal
Right
signal
Range of Applications …
Remote Dental Monitoring
Seizure alert from teeth chatter …
no need for alert dog
Health
Notes: 7. Consider the case of seizures. Today, patients go out with trained dogs that can alert the patient before the onset of a seizure. However, it has been observed that teeth chattering precedes a seizure. EarSense might be able to detect this teeth activity and alert the patient. EarSense may also be used in remote dental monitoring, where vibration data from the teeth can be uploaded for clinical analysis.

## Slide 8
Teeth Gesture,
Location
Infer
Left
signal
Right
signal
Range of Applications …
Type PIN numbers with teeth
Simple hands-free interfaces
UI
Health
Notes: In factories or hospitals ... where workers are wearing gloves or have their hands full ... EarSense can be used to perform simple actions or send commands.
EarSense may be helpful even in everyday use ... a person could type in a PIN number on her phone, or click and scroll while wearing a gloves in winter.

## Slide 9
Teeth Gesture,
Location
Infer
Left
signal
Right
signal
Range of Applications …
UI
Health
Accessibility
Replace Android Switch with EarSense
Notes: Finally, EarSense can help accessibility ... such as by replacing the Android Switch ... which today has to be bought as a separate accessory.

## Slide 10
Teeth Gesture,
Location
Infer
Left
signal
Right
signal
Range of Applications …
UI
Health
Accessibility
Privacy Preserving
Contactless/Hand-free
Ease of interactions
Notes: 10. Importantly, gestures through earphones would be privacy preserving, support contactless and hand-free short interactions and also enhance the usability.

## Slide 11
How?
Notes: So what make EarSense possible?

## Slide 12
Earphone speakers can be re-purposed
as a vibration sensor
We demonstrate:
Notes: 12. Our first pillar is based on the exploitation that COTS earphone speakers can be programmed as vibration sensors

## Slide 13
When external vibrations impinge on the speaker, voltage is produced
Right
signal
Left
signal
Notes: The idea is based on the very basic principle of electromagnetic duality.
If diaphragms of speakers are vibrated through external force, electrical signals are generated in both the channels.

## Slide 14
When external vibrations impinge on the speaker, voltage is produced
This toggles the speaker
as a sensor
(behaving like a microphone)
Right
signal
Left
signal
Notes: 14. Building on this phenomenon, we intend to re-purpose the earphone as a vibration microphone.
In other words, the speaker can act like a microphone ... and hence ... can sense vibrations that conduct through the face and skull.

## Slide 15
Speakers Microphone
Can we toggle automatically?
Notes: But, the system in practice would require an automated toggling between the two.

## Slide 16
Speakers Microphone
Yes, PIN 14-17 can be programmed as either speaker or microphone (called jack re-tasking)
Can we toggle automatically?
Notes: Yes, we can. We do on the fly toggling, which is to and fro conversion of speakers to microphones, using software based jack-retasking on PINs.

## Slide 17
Speakers Microphone
Can we toggle automatically?
And possible in software
(few lines of code change)
Yes, PIN 14-17 can be programmed as either speaker or microphone (called jack re-tasking)
Notes: 17. Pin 14-17 of Realtek Audio codec chips were programmed to act as a microphone is there is no sound being played.

## Slide 18
We demonstrate:
2. Feasibility to infer teeth gestures and locations
Notes: Having captured the signals at two channels, let’s study feasibility of using stereo signals for inferring teeth gestures and locations.

## Slide 19
We demonstrate:
2. Feasibility to infer teeth gestures and locations
EarSense decodes 3 types of teeth gestures across 7 locations
Notes: EarSense decodes 3 types of teeth gestures across 7 locations

## Slide 20
We demonstrate:
2. Feasibility to infer teeth gestures and locations
Left/Middle/Right Tap
3 Taps
2 Vertical Slides
Up-to-Down and Down-to-Up
EarSense decodes 3 types of teeth gestures across 7 locations
2 Horizontal Slides
Left-to-Right and Right-to-Left
Notes: These include 3 location sof tap: left, middle and right. 2 horizontal slides: left-to right and vice versa and 2 vertical slides up-to-down and vice verca.

## Slide 21
We demonstrate:
2. Feasibility to infer teeth gestures and locations
Left/Middle/Right Tap
3 Taps
2 Vertical Slides
Up-to-Down and Down-to-Up
Example: Left Tap
EarSense decodes 3 types of teeth gestures across 7 locations
2 Horizontal Slides
Left-to-Right and Right-to-Left
Notes: An example of left tap in shown in this animation.

## Slide 22
We demonstrate:
2. Feasibility to infer teeth gestures and locations
Left/Middle/Right Tap
3 Taps
2 Vertical Slides
Up-to-Down and Down-to-Up
Example: Left Tap
EarSense decodes 3 types of teeth gestures across 7 locations
2 Horizontal Slides
Left-to-Right and Right-to-Left
Complete teeth gesture inference is a 3 Step Process
Notes: For Earsense, the teeth gesture inference is a 3 step process.

## Slide 23
EarSense: 3 Step Process
1
Teeth Activity
Notes: First, we detect if there is actually a teeth related activity. This classification is based on frequency domain analysis and study of harmonics.

## Slide 24
EarSense: 3 Step Process
1
Teeth Activity
2
Tap/
Slide
Notes: Once we are sure of a teeth activity, we estimate if it is a tap or a slide.

## Slide 25
EarSense: 3 Step Process
1
Teeth Activity
2
Tap/
Slide
Slide
Tap
Spectral Features
Template correlation
Signal durations
Notes: Classification between tap and slide is based on analysis of spectral features, template correlations and signal durations. Taps are impulsive, hence, create a wide band signal.

## Slide 26
3
c
Localization of tap
EarSense: 3 Step Process
Tap Detected
Notes: If a tap is detected, we proceed with it’s localization.

## Slide 27
3
c
Localization of tap
EarSense: 3 Step Process
Tap Detected
Teeth is a dispersive medium
Non-Dispersive
Dispersive
Notes: The challenge here is that, teeth behaves as a dispersive medium. Vibration signals of different frequencies travel at different speed.

## Slide 28
3
Localization of tap
EarSense: 3 Step Process
Tap Detected
(t) !=
Teeth is a dispersive medium
c
Non-Dispersive
Dispersive
Notes: Hence, left and right channels are not delayed versions of each other. Since, signals are not symmetric, standard delay analysis will not suffice here.

## Slide 29
3
Localization of tap
EarSense: 3 Step Process
Tap Detected
Notes: As we saw before, the signals generated during tap are wideband. Because of dispersion, high frequency waves reach first to the ear. We find zero-crossing instances of the received signals at both the channels.

## Slide 30
3
Localization of tap
EarSense: 3 Step Process
Tap Detected
Zero-Crossing Difference
Notes: Differences between zero crossing time at left and right channel is calculate. The intuition is here is that, farther the location of tap from the earphones, more dispersion would be observed. Hence waves would be more stretched out along time axis.

## Slide 31
3
Localization of tap
EarSense: 3 Step Process
Tap Detected
Contraction and relaxation of muscles around ear: Generation of weak cheek waves.
Notes: Also, we exploit occurrence of an interesting phenomenon. Our cheek muscles move more towards the side of teeth activity, right before the teeth strike each other. These contractions and relaxations generate waves.

## Slide 32
3
Localization of tap
EarSense: 3 Step Process
Tap Detected
Contraction and relaxation of muscles around ear: Generation of weak cheek waves.
Notes: We measure energy of these weak waves, right before detection of a tap and report about the probable location of the activity.

## Slide 33
3
Localization of tap
EarSense: 3 Step Process
Tap Detected
EarSense
Zero-Crossing Difference
Cheek Waves Dominance
TDoA of low frequencies
L/M/R Tap
Notes: As a whole, tap detection uses fusion of 3 techniques on the stereo signals: zero-crossing differences, dominance of cheek waves and time-difference of arrival of lower frequencies. Using a joint voting Earsense reports wether middle, left or right tap was done.

## Slide 34
3
Tracking Slide
EarSense: 3 Step Process
Location of friction shifts from left to right
Notes: We exploit a differentiating opportunity with the slides. As can be seen in the animation, the location of friction shifts during a slide.

## Slide 35
Location of friction shifts from left to right
3
Tracking Slide
EarSense: 3 Step Process
Delays between the channels changes
Notes: This change of point of contact leads to variation in relative delays between left and right channels, as the teeth move from an end to the other.

## Slide 36
3
Tracking Slide
EarSense: 3 Step Process
Delays between the channels shifts
Delays profiles are created
Notes: Hence, we designed a delay profile based classifier to identify among the 4 slides. We can use delay vs time profile to classify among horizontal and vertical slides.
The delays changes both magnitude and sign as the slide progresses. While vertical slides have near 0 delays, the delays for horizontal slides spans across two extremes..

## Slide 37
EarSense Evaluation
Uniform performance across users
Notes: Earsense was evaluated across multiple earphones and target uses. Our evaluation proves that the processing chain which is not only accurate but scalable as well. The performance is uniform across different users for all the gestures.

## Slide 38
Off-the-shelf earphones can
sense facial surface vibrations?
Vibration signals can be analyzed
to infer teeth gestures and their locations?
1
2
This paper develops EarSense and shows:
Teeth Gesture,
Location
Infer
Left
signal
Right
signal
Infer
Left
signal
Notes: To conclude, this paper claims that we can use off the shelf earphones to sense facial surface vibrations. These vibrations signals can give idea about teeth gestures and even the location of the corresponding activity.

## Slide 39
We foresee using Earbuds to SMS and in-app OTPs
Notes: I would like to conclude with a demo video which we foresee as one of the uses cases of Earsense. While accessing online portals, when we encounter two factorauthentication we are mandated to enter OTP codes either through SMS or through a dedicated applications. How about replacing number with teeth gestures. Wont’t it enhance usability and increase the adoption of TFA which is lower than 25%! We believe it will.

## Slide 40
Much more in the paper …
Thanks.
Zhijian
Yu-Lin
Haitham
Romit
Jay
Notes: We request to have a look at our paper for a details. We would be glad to disxuss and push this rapidly evolving field around earable computing.