## Slide 1: Closing the Gaps in Inertial Motion Tracking
Sheng Shen, Mahanth Gowda, Romit Roy Choudhury

## Slide 2
Inertial Measurement Unit (IMU)
Gyroscope
Accelerometer
Magnetometer

## Slide 3
Inertial Measurement Unit (IMU)
Gyroscope
Accelerometer
Magnetometer

## Slide 4
Inertial Measurement Unit (IMU)
Gyroscope
Accelerometer
Magnetometer
Wide applications in motion tracking

## Slide 5
Motion
Tracking
Algorithm
IMU Data
3D Trajectory
Lot of work in inertial motion tracking
Open problem in mobile computing

## Slide 6
Motion
Tracking
Algorithm
IMU Data
3D Trajectory
Lot of work in inertial motion tracking
Open problem in mobile computing
This paper doesn’t solve it either … however, makes progress

## Slide 7
Motion
Tracking
Algorithm
IMU Data
3D Trajectory
Lot of work in inertial motion tracking
Open problem in mobile computing
This paper doesn’t solve it either … however, makes progress
Am struggling to explain our algorithm … so will start from scratch

## Slide 8
One Prerequisite Slide: Rotation Matrices
X:
Rotation is a function
Y:
90°
X:
Y:
Mathematically, rotation is a matrix
Same for 3D Rotation

## Slide 9
MUSE: Our Goal is 3D Localization
Map
3D Trajectory
Algorithm
Initial Location
IMU = Accel + Gyro + Mag

## Slide 10
Let’s Understand the Inputs
Initial Location
Algorithm
Zoom into IMU data:
Accel.
Gyro.
Mag.
(Linear Acceleration)
(Angular Velocity)
(Earth’s Magnetic North)
Delta rotation in unit time
IMU = Accel + Gyro + Mag

## Slide 11
Can we solve localization with these inputs?
Initial Location
Algorithm
?
IMU = Accel + Gyro + Mag

## Slide 12
One possibility is:
Initial Location
IMU
Accel., Gyro., Mag.
But there is one BIG problem:
Accel. is in local reference frame

## Slide 13
But there is one BIG problem:
Accel. is in local reference frame

## Slide 14
As an analogy
What is
Frontwards
Rightwards
Upwards
w.r.t. the earth?
Accelerating
: Frontwards
: Rightwards
: Upwards
Map
3D Trajectory
New Delhi Airport
But there is one BIG problem:
Accel. is in local reference frame

## Slide 15
This makes orientation necessary

## Slide 16
Plane’s Own
What is 3D orientation?
Orientation is the 3D rotation needed to make:
Right
Front
Up
This makes orientation necessary

## Slide 17
What is 3D orientation?
Right: East
Front: North
Up: Vertical
This makes orientation necessary
Plane’s Own
Orientation is the 3D rotation needed to make:

## Slide 18
So, how will orientation solve the problem?
Initial Location
IMU (Local)
What we need to do is:
3D Orient.
Accel.
Gyro.
Mag.
IMU (Global)
Accel.
+
So 3D orientation is the key.

## Slide 19
So how to get 3D orientation?
2 Main Opportunities:
1. Gravity
2. Magnetic North
Both measurable by IMU
Key idea: What rotation is needed such that
      Gravity is exactly in my downward direction
      North is exactly in my frontward direction

## Slide 20
So how to get 3D orientation?
Key idea: What rotation is needed such that
      Gravity is exactly in my downward direction
      North is exactly in my frontward direction

## Slide 21
So how to get 3D orientation?
Gravity
Downward
Gravity says a lot about orientation, but not sufficient
Tilt is determined (2 out of 3 DoFs)
Key idea: What rotation is needed such that
      Gravity is exactly in my downward direction
      North is exactly in my frontward direction

## Slide 22
So how to get 3D orientation?
North
Frontward
My orientation
Tilt + Heading is determined (all 3 DoFs)
Key idea: What rotation is needed such that
      Gravity is exactly in my downward direction
      North is exactly in my frontward direction

## Slide 23
So is Gravity + North enough to get 3D Orientation?
Only when object is static … but not otherwise. Why?

## Slide 24
So is Gravity + North enough to get 3D Orientation?
Only when object is static … but not otherwise. Why?
Because any motion of the object will reflect
in the accelerometer … thereby
polluting the gravity estimate

## Slide 25
So how to get 3D orientation? (Another idea)
Another Idea for Orientation:
Integrate angular velocity from gyro
Initial Orientation
+
New Orientation
=
But gyro drifts, so only useful in short time scales
(at time t)

## Slide 26
State of the art today: Sensor Fusion
Time
Static
Moving
Static
Moving
Static
Moving
Rely mostly on gravity + North
Rely mostly on gyro integration
……
Always know 3D orientation

## Slide 27
Getting back to our goal
Initial Location
IMU (Local)
3D Orient.
Accel.
Mag.
IMU (Global)
Accel.
+
Static?
3D Orient.
Y
Gyro.
N
Location

## Slide 28
Getting back to our goal
Initial Location
IMU (Local)
3D Orient.
Accel.
Mag.
IMU (Global)
Accel.
+
Static?
3D Orient.
Y
Gyro.
N
Location
Main take away: Gravity is the main anchor for 3D orientation

## Slide 29
But what if object is not often static
This paper: MUSE

## Slide 30
What does MUSE do?
Time
Static
Moving
Static
Moving
Use magnetometer as our main anchor
Joint estimation of orientation and location
MUSE = Estimate 3D Orientation even for moving object

## Slide 31
What does MUSE do?
Time
Static
Moving
Static
Moving
Use magnetometer as our main anchor
Joint estimation of orientation and location
MUSE = Estimate 3D Orientation even for moving object

## Slide 32
From: Wikipedia
Earth’s North Pole
Earth’s South Pole

## Slide 33
From: Wikipedia
Earth’s North Pole
Earth’s South Pole
Magnetic Field Direction on Earth Surface

## Slide 34
Y: North
X: East
Z: Up
Global Reference Frame
Magnetic Field Direction
Earth’s Magnetic Field as Main Anchor

## Slide 35
Horizontal Plane
Magnetic Field Direction
North
Earth’s Magnetic Field as Main Anchor
This vector is not influenced by motion!
Let’s make it our main anchor

## Slide 36
Magnetic Field Direction
Main Anchor
Earth’s Magnetic Field as Main Anchor

## Slide 37
Earth’s Magnetic Field as Main Anchor
Three questions:
What does it say about my orientation?
Magnetometer’s resolution is low …
How to know x, y, z of earth magnetic field?

## Slide 38
Earth’s Magnetic Field as Main Anchor
Three questions:
What does it say about my orientation?
Magnetometer’s resolution is low …
How to know x, y, z of earth magnetic field?

## Slide 39
Z: Outward
Y: Front
X: Right
[Local]
Actual Measurement (from magnetometer)
Actual vs. Inferred Measurement
Z: Outward
Y: Front
X: Right
[Local]
Inferred Measurement (inferred from orientation estimation)

## Slide 40
Z: Outward
Y: Front
X: Right
[Local]
Actual Measurement (from magnetometer)
Actual vs. Inferred Measurement
Z: Outward
Y: Front
X: Right
[Local]
Inferred Measurement (inferred from orientation estimation)
and are equal, if our orientation is estimated perfectly …

## Slide 41
Z: Outward
Y: Front
X: Right
[Local]
Actual vs. Inferred Measurement
2-DoF Orientation Drift == How off is from

## Slide 42
Z: Outward
Y: Front
X: Right
[Local]
Actual vs. Inferred Measurement
2-DoF Orientation Drift == How off is from

## Slide 43
Z: Outward
Y: Front
X: Right
[Local]
Actual vs. Inferred Measurement
New Orientation = Old Orientation +

## Slide 44
Actual vs. Inferred Measurement
New Orientation = Old Orientation +
Orientation(t) = Orientation(t-1) +
Orientation(t) = Orientation(t) +
Gyroscope:
Magnetometer:

## Slide 45
Earth’s Magnetic Field as Main Anchor
Three questions:
What does it say about my orientation?
Magnetometer’s resolution is low …
How to know x, y, z of earth magnetic field?

## Slide 46
Earth’s Magnetic Field as Main Anchor
How to know x, y, z of earth magnetic field?
Obtain GPS address and check the database is one option …
A easier way is to utilize pause opportunities
Known when object is static

## Slide 47
Evaluation

## Slide 48
GyroOnly | Only uses gyroscope integration, assuming initial orientation is known
ComplemFilter | (Option 1) Use low-pass filter on acceleration
A3 | (Option 2) Calibrate using “good” opportunities
MUSE | Our algorithm
Comparison Baselines
Ground Truth: Periodically bringing the phone to the same orientation, and excluding those moments from calibration opportunities

## Slide 49
Natural Activities

## Slide 50
A Sample Trace

## Slide 51
OK, we have 3D Orientation now… how to estimate location?

## Slide 52
OK, we have 3D Orientation now… how to estimate location?
Initial Location
IMU (Local)
3D Orient.
Accel.
Gyro.
Mag.
IMU (Global)
Accel.
+

## Slide 53
OK, we have 3D Orientation now… how to estimate location?
Initial Location
IMU (Local)
3D Orient.
Accel.
Gyro.
Mag.
IMU (Global)
Accel.
+
Localization impossible if
accelerometer has any noise … why?

## Slide 54
Initial Location
IMU (Local)
3D Orient.
Accel.
Gyro.
Mag.
IMU (Global)
Accel.
+
Motion models can bound location error

## Slide 55
Initial Location
IMU (Local)
3D Orient.
Accel.
Gyro.
Mag.
IMU (Global)
Accel.
+
Motion model as priors
Motion models can bound location error

## Slide 56
Initial Location
IMU (Local)
3D Orient.
Accel.
Gyro.
Mag.
IMU (Global)
Accel.
+
Motion model as priors
MUSE uses this motion model to
jointly estimate both { orientation + location }

## Slide 57
Initial Location
IMU (Local)
3D Orient.
Accel.
Gyro.
Mag.
IMU (Global)
Accel.
+
Motion model as priors
MUSE uses this motion model (in a particle filter) to
jointly estimate both { orientation + location }

## Slide 58
OK, we have 3D Orientation now… how to estimate location?
Initial Location
IMU (Local)
3D Orient.
Accel.
Gyro.
Mag.
IMU (Global)
Accel.
+
Motion model as priors

## Slide 59
MUSE Localization Error
(cm)
Fits motion model the best
Motion model breaks

## Slide 60
This paper
Conclusion
Orientation
Location
Joint estimation of orientation and location
Use magnetometer as a new “gravity” sensor
Conventional Systems